## Slide 1: White Gull Creek MESH Point Scale Configuration Exercise
January 20, 2020

## Slide 2: Pre-modelling steps
Set up the project folders
  Git tracking
  See https://github.com/MESH-Model/MESH_Project_Template for an example
  Can clone the folders I have set up from here: https://github.com/MESH-Model/MESH_Whitegull
  Note: when setting up MESH, it is helpful to have an existing version of the model with a similar configuration to yours as a starting point for file layout, default parameters, etc.
Familiarize yourself with the site
Define modelling goals

## Slide 3: Notes about Point Mode
Old way:
  Setting up the MESH_drainage_database.r2c file with one active grid cell to create an “effective” point mode
New way:
  Use the newest interim release of MESH (r1593) (https://wiki.usask.ca/display/MESH/Interim+releases)
  In MESH_run_options.ini set RUNMODE = noroute and SHDFILEFLAG = 2
  In the MESH_parameters_CLASS.ini file, set the number of grids (NL) to 1
  No longer need to have the MESH_drainage_database.r2c, MESH_input_streamflow.txt, or MESH_input_reservoir.txt files
  See https://wiki.usask.ca/display/MESH/RUNMODE

## Slide 4: Configure the model
Note: the following steps are somewhat iterative, as the choices or changes made in model configuration may need to be reflected in multiple files
Meteorological forcing data files
  See this MESH wiki page for more details: https://wiki.usask.ca/display/MESH/Meteorological+Input
  .csv files may be used for point mode
    Only 1 column needed since only 1 GRU in the basin
  See the file: Code/ForcingFilePrep.ipynb
    Note: I manually downloaded the observed data from WISKI desktop app as WISKI Tools python code was not working for BER_OBS_11 (Modelling dataset)

## Slide 5: Configure the model
Select parameters for the CLASS and hydrology .ini files
  Make sure to use the “version 2.0” of they hydrology.ini file (https://wiki.usask.ca/pages/viewpage.action?pageId=1176797394)
  Additional parameters need to be defined if using PDMROF or FROZEN algorithms
  Some of thehydrology parameters in the CLASS file not used for flat CLASS
  Note the different sections of the CLASS.ini file (see next slide if needed)
  See the wiki for more details about the parameters:
    https://wiki.usask.ca/display/MESH/MESH_parameters_CLASS.ini
    https://wiki.usask.ca/display/MESH/MESH_parameters_hydrology.ini
    https://wiki.usask.ca/display/MESH/MESH+Parameter+Selection

## Slide 6: Configure the model
Prepare the run options file (MESH_input_run_options.ini)
  Appropriate flags
    Ex. IWF (runoff algorithm used), IPCP (precip. Phase partitioning), SHDFILEFLAG, RUNMODE, FROZENSOILINFILFLAG
  Start and stop date and times
    Note: model must start on or after the first timestep of the forcing data (specified in CLASS.ini)
  https://wiki.usask.ca/display/MESH/MESH_input_run_options.ini

## Slide 7: Configure the model
Set up run scripts
  For this example, see Model/Config_PointScale/RunAll.sh
    Runs a makefile to process the driving data
    Puts a symbolic link to the driving data in the folder
    Compiles the model
    Run the model
    Process the outputs and generate image files of the graphs
Run the model

## Slide 8: MESH Model Files – CLASS.ini
Header Info
Vegetation Parameters
Hydraulic Parameters
Soil Texture Parameters
Initial Prognostic Values

## Slide 9: MESH Model Files – CLASS.ini
Vegetation Parameters
Needleleaf Broadleaf Crops Grass Urban/barren/
impervious
Needleleaf Broadleaf Crops Grass

## Slide 10: MESH Model Files – CLASS.ini
Layer 1 Layer 2 Layer 3 Layer 4
Soil Texture Parameters

## Slide 11: MESH Model Files – CLASS.ini
Initial Prognostic Values
One value of soil temperature and moisture for each layer

## Slide 12: MESH Model Files – CLASS.ini
Starting hour, minute, day (julian), and year of the meteorological input files

## Slide 13: General Notes
Just because there is a value in an input file doesn’t mean it is being used by the model
  Need to consider the flags used (run_options.ini)
The MESH wiki is a great resource, but exercise caution as some information is out-of-date, and the information is not exhaustive
  The “MESH Input Files” pages are especially useful
  Try the search bar in addition to the page tree navigation
  If there’s something you want to do / know regarding the model, ask Dan
Keep notes about the model setup choices made in “ReadMe.md” files in the project folder
  “Breadcrumbs” for yourself to remember what you did
  Helpful for distinguishing different configurations
  Document justification of your choices to your supervisor and when writing your thesis or publishing papers